## Slide 1: ECEN689 – Project #3 RF Signal Strength Data Collection Tool
April 15, 2016
John Lusher II, P.E.
Notes: This is an example of a notes page.
Please add as much info here to clearly communicate this slide to a non-engineering individual.
Go to ‘View’ and click on ‘Notes Page’

## Slide 2: Purpose
Captures RSSI from XBee Pro radio interface with Teensy MCU.
Captures IMU orientation of phone
Communicate stored data to SQL Server
Be stable and easy to use

## Slide 3: APIs, Technologies, and Main Classes
  Google Map API
    Googles’ API for interfacing their Google Map and integrate into an Android Application
  MySQL Connector
    Provides interface to connect to MySQL database and run SQL commands to insert new records and query records.
  USB Serial Connector
    Provides USB to Serial interface for Android Applications. Allows application to open port and create a listener to receive streaming input data, in this application the RSSI data.
  Latitude and Longitude
    Class to generate latitude and longitude based upon a starting location and given a distance and bearing. This is used for determine an area for the map viewer to pull data from the SQL database.
  RF Field SQL Database
    Class to provide simple interface to SQL database being provided functions to connect and add new data based upon the RF Data class.
  RF Data Class
    Simply the class in which all data for a record is stored, this includes the IMU data, RSSI, sample date, Lat/Long
  Telephony Manger / Phone State
    Provides the ability to get the RSSI of the various bands available to the cellular radio.
  Location Manager
    Provides the ability to get the geo-location of the device.
  Sensor Manager
    Provides the ability to get the sensor (IMU) information for the device. In this case we are interested in the Yaw, Pitch, and Roll.

## Slide 4: Google Maps Implementation
@Override protected void onCreate(Bundle savedInstanceState) { super.onCreate(savedInstanceState); setContentView(R.layout.activity_maps); // Obtain the SupportMapFragment and get notified when the map is ready to be used. SupportMapFragment mapFragment = (SupportMapFragment) getSupportFragmentManager() .findFragmentById(R.id.map); mapFragment.getMapAsync(this); }
@Override public void onMapReady(GoogleMap googleMap) { mMap = googleMap; /// Add a marker in EIC and move the camera /// We will need to hack this to work with other lat/long values to be displayed LatLng eic = new LatLng(30.618708, -96.341558); mMap.addMarker(new MarkerOptions().position(eic).title("EIC")); mMap.moveCamera(CameraUpdateFactory.newLatLngZoom(eic, 19)); mMap.setOnMapClickListener(this); // Calls function to update the map on the container UpdateMap((float) eic.latitude, (float) eic.longitude, 1000F); }

## Slide 5: Serial Port Listener for Teensy LC on Android
//------------------------------------------------------------------------------------------------------------------ // SERIAL PORT LISTENER //------------------------------------------------------------------------------------------------------------------ private final SerialInputOutputManager.Listener mListener = new SerialInputOutputManager.Listener() { private final static String RXID = "Receive ID"; private final static String TXID = "Transmit ID"; private final static String RSSI = "RSSI"; @Override //------------------------------------------------------------------------------------------------------------------ /** * @fun SerialInputOutputManager.Listener:onRunError * @brief On Run Error */ public void onRunError(Exception e) { } @Override //------------------------------------------------------------------------------------------------------------------ /** * @fun SerialInputOutputManager.Listener:onNewData * @brief On New Data */ public void onNewData(final byte[] data) { try { // Append data to the incomming string buffer // Read data from Teensy device (based upon project by Paul Crouther) - JSON Object being streamed // to serial port at 9600 bps, includes IDs and RSSI, Note: RSSI is pos, actually is negative. String newrx = new String(data, "UTF-8"); JSONObject serialJSONObj = new JSONObject(newrx); CurrenSample.XbeeID = serialJSONObj.getInt(RXID); CurrenSample.DeviceID = serialJSONObj.getInt(TXID); XBeeRSSI = -1.0 * serialJSONObj.getDouble(RSSI); } catch (Exception e) { } } };

## Slide 6: References
  Project #1 and Project #2 from ECEN489/689 Class.
  Google API
  Example / test projects provided by Google (i.e. Google Maps, Hello World)